## Slide 1: Hypha ROS RaceCar Workshop 2017-06
Website: https://hypharosworkshop.wordpress.com/contact/
FB Page: https://www.facebook.com/HyphaROS/
Email: hypha.ros@gmail.com
Lecturer : HaoChih, LIN
林浩鋕

## Slide 2
Lecturer: HaoChih, LIN
https://hypharosworkshop.wordpress.com/
Copyright © 2017 Hypha ROS Workshop. All rights reserved
6/10 (週六) |  |  | 6/11 (週日) |  | 
時段 | 課程 | 教室 | 時段 | 課程 | 教室
10:00 12:00 | 課程介紹 2D SLAM | 綜合教學大樓 | 09:00 12:30 | Navigation & Amcl Simulation | 綜合教學大樓
12:00 13:30 | 中午休息 (自行外出用餐) |  | 12:30 14:00 | 中午休息 (自行外出用餐) | 
13:30 15:30 | Laser Odom EKF (IMU+Odom) | 綜合教學大樓 | 14:00 15:30 | System Integration | 工學院交誼廳
休息10分鐘 |  |  |  |  | 
15:40 18:30 | Base Controller & Path following | 綜合教學大樓 | 15:40 16:50 | Final Testing & Debugging | 工學院交誼廳
18:30 20:00 | 晚餐時間 (自行外出用餐) |  | 17:00 18:00 | Competition | 工學院交誼廳
20:00 21:30 | 硬體Debug (此時段非必要,依需求) | 綜合教學大樓 | 18:00 ~ | 工作坊結束 | 
Notes: 工作坊 基本介紹 （我們是誰）
兩日注意事項 （貴重物品 垃圾 午餐 晚餐 水 廁所 debug時間 隔天最終場地等）
不得錄音 錄影 可以拍照
code部份 都公開
有問題可以發問 但因為時間有限 所以太過細節部份 建議debug時段提問

## Slide 3
Lecturer: HaoChih, LIN
https://hypharosworkshop.wordpress.com/
Copyright © 2017 Hypha ROS Workshop. All rights reserved
ROS X Odroid (Basic operation)
2D SLAM algorithms implementation & comparsion
  gmapping
  hector slam
  mrpt-icp
Odometry Estimation
  laser Odom (rf2o pkg)
  fused with IMU (by robot_localization pkg)
  gmapping based on fused odom
Communication & Control
  rosserial arduino
  Teleop testing
  L1 controller
  Path planning test (movebase)
Hardware Debug [optional]

## Slide 4
Lecturer: HaoChih, LIN
https://hypharosworkshop.wordpress.com/
Copyright © 2017 Hypha ROS Workshop. All rights reserved
ROS X Odroid (Basic operation)

## Slide 5
Lecturer: HaoChih, LIN
https://hypharosworkshop.wordpress.com/
Copyright © 2017 Hypha ROS Workshop. All rights reserved
ROS X Odroid (Basic operation)
[desktop] Download pkg from Hypha-ROS github
  $ cd catkin_ws/src
  $ git clone https://github.com/Hypha-ROS/hypha-racecar
[desktop] SSH/Remmina to Odroid
  Wifi configuration (ad-hoc pw: 1234567890, SSID: hypha0X)
  Ethernet configuration
  ROS multi-machine env setting (in hypha-racecar/document/ROS_multiMachine/)
  ssh → $ ssh odroid@192.168.XX.1 (pw: hypharos)
  remmina (vino pw: 0000)
[odroid] Modify wifi setting
  sudo gedit /etc/network/interfaces (pw: hypharos)
  ROS multi-machine env setting (in bashrc)

## Slide 6
Lecturer: HaoChih, LIN
https://hypharosworkshop.wordpress.com/
Copyright © 2017 Hypha ROS Workshop. All rights reserved
ROS X Odroid (Basic operation)
[desktop] image backup
  Read: In hypha-racecar/document/commands/
  $ sudo fdisk -l /dev/sdb
  $ sudo dd if=/dev/sdb bs=512 count=29624319 of=~/HyphaROS_xu4_kinetic_20170610.img
  Write: Ubuntu GUI
[odroid] Change git config
  $ cd catkin_ws/src
  $ git config --global user.name "YOUR NAME"
  $ git config --global user.email YOUR EMAIL
  $ git config --list (to ckeck setting)

## Slide 7
Lecturer: HaoChih, LIN
https://hypharosworkshop.wordpress.com/
Copyright © 2017 Hypha ROS Workshop. All rights reserved
ROS X Odroid (Basic operation)
[odroid] Create your own ROS pkg
  $ cd catkin_ws/src
  $ catkin_create_pkg PACKAGE_NAME geometry_msgs move_base tf roscpp rospy std_msgs visualization_msgs
[odroid] Udev Setting
  $ lsusb (check the idV and idP of each component)
  Select one for finding the ISB port
  $ ls dev/ttyACM or ttyUSB
  $ udevadm info -a /dev/ttyUSB0
  $ sudo gedit /etc/udev/rules.d/99-NAME.rule
  ⇒ KERNEL=="ttyUSB*", ATTRS{idProduct}=="ea60", ATTRS{idVendor}=="10c4", MODE="666", ATTRS{devpath}=="1.2.1.2", SYMLINK+="rplidar

## Slide 8
Lecturer: HaoChih, LIN
https://hypharosworkshop.wordpress.com/
Copyright © 2017 Hypha ROS Workshop. All rights reserved
ROS X Odroid (Basic operation)
[concept] Establishing a topic connection
  Subscriber starts.
  Publisher starts.
  Subscriber registers with the Master. (XMLRPC)
  Publisher registers with the Master. (XMLRPC)
  Master informs Subscriber of new Publisher. (XMLRPC)
  Subscriber contacts Publisher to request a topic connection and negotiate the transport protocol. (XMLRPC)
  Publisher sends Subscriber the settings for the selected transport protocol. (XMLRPC)
  Subscriber connects to Publisher using the selected transport protocol. (TCPROS, etc...)
figure source: http://wiki.ros.org/ROS/Technical%20Overview

## Slide 9
Lecturer: HaoChih, LIN
https://hypharosworkshop.wordpress.com/
Copyright © 2017 Hypha ROS Workshop. All rights reserved
ROS X Odroid (Basic operation)
[tool] rostopic commands
  rostopic bw display bandwidth used by topic
  rostopic delay display delay for topic which has header
  rostopic echo print messages to screen
  rostopic find find topics by type
  rostopic hz display publishing rate of topic
  rostopic info print information about active topic
  rostopic list print information about active topics
  rostopic pub publish data to topic
  rostopic type print topic type
[tool] rosbag commands
  rosbag record -a
  rosbag record --duration=5m
  rosbag play --clock recorded1.bag

## Slide 10
Lecturer: HaoChih, LIN
https://hypharosworkshop.wordpress.com/
Copyright © 2017 Hypha ROS Workshop. All rights reserved
ROS X Odroid (Basic operation)
[tool] roslaunch
  http://wiki.ros.org/roslaunch/XML
  See example
[tool] TF
  http://wiki.ros.org/tf
  http://wiki.ros.org/tf/Tutorials/Introduction%20to%20tf
  http://wiki.ros.org/navigation/Tutorials/RobotSetup/TF
  http://wiki.ros.org/urdf/Tutorials/Using%20urdf%20with%20robot_state_publisher#Create_the_URDF_File
  $ tf_echo <source_frame> <target_frame>
  static_transform_publisher (See example)
<launch>
<node pkg="tf" type="static_transform_publisher" name="base2laser" args="1 0 0 0 0 0 base_link laser_link 10" />
</launch>

## Slide 11
Lecturer: HaoChih, LIN
https://hypharosworkshop.wordpress.com/
Copyright © 2017 Hypha ROS Workshop. All rights reserved
ROS X Odroid (Basic operation)
[concept] TF
  http://www.ros.org/reps/rep-0105.html
figure source: http://library.isr.ist.utl.pt/docs/roswiki/hector_slam(2f)Tutorials(2f)SettingUpForYourRobot.html
figure source: http://www.ros.org/reps/rep-0105.html

## Slide 12
Lecturer: HaoChih, LIN
https://hypharosworkshop.wordpress.com/
Copyright © 2017 Hypha ROS Workshop. All rights reserved
ROS X Odroid (Basic operation)
[tool] rviz
  See example ($ roslaunch hypha_racecar desktop_gmapping.launch)
[tool] rqt
  See example

## Slide 13
Lecturer: HaoChih, LIN
https://hypharosworkshop.wordpress.com/
Copyright © 2017 Hypha ROS Workshop. All rights reserved
ROS X Odroid (Basic operation)
ROS Technical documents
  [roslaunch] http://wiki.ros.org/roslaunch/XML
  [rosbag] http://wiki.ros.org/rosbag/Commandline
  [rostopic] http://wiki.ros.org/rostopic
  [ros intro] http://wiki.ros.org/ROS/Introduction
  [ros concept] http://wiki.ros.org/ROS/Concepts
  [REP] http://www.ros.org/reps/rep-0000.html
  http://wiki.ros.org/ROS/Technical%20Overview
  http://docs.ros.org/indigo/api/catkin/html/index.html
  http://wiki.ros.org/Remapping%20Arguments
  http://wiki.ros.org/ROS/Master_Slave_APIs

## Slide 14
Lecturer: HaoChih, LIN
https://hypharosworkshop.wordpress.com/
Copyright © 2017 Hypha ROS Workshop. All rights reserved
2D Laser SLAM

## Slide 15
Lecturer: HaoChih, LIN
https://hypharosworkshop.wordpress.com/
Copyright © 2017 Hypha ROS Workshop. All rights reserved
Gmapping
  needs external odom (in our case: laser odom fused with imu0)
  Rao-Blackwellized Particle Filter (RBPF)
  Loop closure
Hector SLAM
  Gauss-Newton approach
  External odom is not necessary
  No loop closure
  Requires high quality sensor (e.g. UTM-30LX)
  Supports EKF fusion (imu)
MRPT-ICP SLAM
  ICP algorithm
  For small to mid-sized maps
  External odom is not necessary
2D Laser SLAM

## Slide 16
Lecturer: HaoChih, LIN
https://hypharosworkshop.wordpress.com/
Copyright © 2017 Hypha ROS Workshop. All rights reserved
Gmapping
  $ roslaunch hypha_racecar desktop_gmapping.launch
MRPT-ICP SLAM
  $ roslaunch hypha_racecar desktop_icp_mapping.launch
Hector SLAM
  $ roslaunch hypha_racecar Test_hector_rplidar.launch
2D Laser SLAM
gmapping (laser odom)
mrpt icp
hector slam

## Slide 17
Lecturer: HaoChih, LIN
https://hypharosworkshop.wordpress.com/
Copyright © 2017 Hypha ROS Workshop. All rights reserved
Laser Odom (EKF IMU)

## Slide 18
Lecturer: HaoChih, LIN
https://hypharosworkshop.wordpress.com/
Copyright © 2017 Hypha ROS Workshop. All rights reserved
Odometry resource selection
Wheel encoder
  Most reliable (in low speed)
  Slip/Drifting Issue
  Custom codes
Laser odometry
  Performance depends on laser resolution/environment features
  Good estimates in translation, awful in rotation
  Better system portability
Visual Odometry (or Visual Inertial Odometry)
  Low robust
  High computational loading
  Case by case tuning
  Highly depends on sensor type/quality
Laser Odom (EKF IMU)

## Slide 19
Lecturer: HaoChih, LIN
https://hypharosworkshop.wordpress.com/
Copyright © 2017 Hypha ROS Workshop. All rights reserved
rf2o laser odom package
  http://mapir.isa.uma.es/mapirwebsite/index.php/mapir-downloads/papers/217
  range flow constraint equation
  Iteratively Reweighted Least Squares (IRLS)
Laser Odom (EKF IMU)
figure source:
Planar Odometry from a Radial Laser Scanner. A Range Flow-basedApproach

## Slide 20
Lecturer: HaoChih, LIN
https://hypharosworkshop.wordpress.com/
Copyright © 2017 Hypha ROS Workshop. All rights reserved
Problem of rf2o
  Performance of rf2o is bad in rotation behavior
  Needs external measurement to estimate yaw motion (gy85)
ROS EKF Package
  robot_pose_ekf
    move_base built-in pkg
    for 2D, low flexibility
  robot_localization
    all params are adjustable, well documented
    3D model based
    supports multi-sensors (including GPS, imu, vo, etc)
  ethzasl_msf
    ESKF architecture (imu derived model)
    good for VO measurement
    best choice for drone
Laser Odom (EKF IMU)

## Slide 21
Lecturer: HaoChih, LIN
https://hypharosworkshop.wordpress.com/
Copyright © 2017 Hypha ROS Workshop. All rights reserved
robot_localization pkg
  http://wiki.ros.org/robot_localization
  https://github.com/cra-ros-pkg/robot_localization
  [document] http://docs.ros.org/indigo/api/robot_localization/html/index.html
  [video] https://vimeo.com/142624091
  All state estimation nodes track the 15-dimensional state of the vehicle:
  Implementation (See example file: "hypha_ekf_params.yaml") Vx, Vy from rf2o, yaw from imu, custom covariance settings
Laser Odom (EKF IMU)

## Slide 22
Lecturer: HaoChih, LIN
https://hypharosworkshop.wordpress.com/
Copyright © 2017 Hypha ROS Workshop. All rights reserved
IMU yaw reading
  [arduino] http://wiki.ros.org/razor_imu_9dof
  [odroid] gy85 with modified pySerial code
  Using gyro_z raw data for integration directly instead of output data from ekf
  See example (file: imu_auto.py)
Ros bag Testing
  Try to modify ekf param file (desktop_gmapping.launch)
Realtime onboard testing
  Test_laser_odom.launch
  Test_gmapping.launch
Laser Odom (EKF IMU)

## Slide 23
Lecturer: HaoChih, LIN
https://hypharosworkshop.wordpress.com/
Copyright © 2017 Hypha ROS Workshop. All rights reserved
Laser Odom (EKF IMU)

## Slide 24
Lecturer: HaoChih, LIN
https://hypharosworkshop.wordpress.com/
Copyright © 2017 Hypha ROS Workshop. All rights reserved
Communication & Control

## Slide 25
Lecturer: HaoChih, LIN
https://hypharosworkshop.wordpress.com/
Copyright © 2017 Hypha ROS Workshop. All rights reserved
rosserial arduino
  [setup] http://wiki.ros.org/rosserial_arduino/Tutorials/Arduino%20IDE%20Setup
  racecar_uno.ino [hypha-racecar/document/arduino/racecar_uno/]
  racecar_uno_hsp.ino for HSP model car
Teleop testing
  [rosrun] $ rosrun rosserial_python serial_node.py /dev/uno
  [rosrun] $ rosrun rosserial_python serial_node.py _port:=/dev/uno _baud:=57600
  [roslaunch]
<!-- Arduino -->
<node pkg="rosserial_python" type="serial_node.py" name="serial_node">
<param name="port" value="/dev/uno"/>
<param name="baud" value="57600"/>
</node>
  $ rosrun hypha_racecar racecar_teleop.py
Communication & Control

## Slide 26
Lecturer: HaoChih, LIN
https://hypharosworkshop.wordpress.com/
Copyright © 2017 Hypha ROS Workshop. All rights reserved
L1 controller
  paper: http://acl.mit.edu/papers/KuwataTCST09.pdf
  paper: http://acl.mit.edu/papers/KuwataGNC08.pdf
Communication & Control

## Slide 27
Lecturer: HaoChih, LIN
https://hypharosworkshop.wordpress.com/
Copyright © 2017 Hypha ROS Workshop. All rights reserved
L1 controller Implemenation
  [source code] L1_controller.cpp
  Speed control:
  current version => constant spped
Path planning test
  RACECAR_amcl_nav.launch
Communication & Control
figure source: Yoshiaki Kuwata, Motion Planning in Complex Environments using Closed-loop Prediction

## Slide 28
Lecturer: HaoChih, LIN
https://hypharosworkshop.wordpress.com/
Copyright © 2017 Hypha ROS Workshop. All rights reserved
Hardware Debug [optional]